## Slide 1: NEMS planning
LBHB Lab Meeting
June 14, 2017

## Slide 2: Next month
Stephen’s schedule next month
  Out June 19-29
  Back 29-30
  Out again July 3-14
  Back Monday July 17
  Skype (svdavid1), Google Hangout?
Surgery
  Implant SPF animal for Jesyin pilots.
  MRB surgery suit closed, IACUC has approved use of Knight Inst. suite on LBRB 1st floor.
  Need card key access, need to schedule with Elizabeth Le and Traci Schaller

## Slide 3: NEMS – Neural Encoding Model System
Wu et al. 2006; Thorson & David 2015
Time-varying response as a function of the incoming stimulus:

## Slide 4: Core – the model engine
Basic model:
(input data)
“Engine”:
(starting point)
Load module – or make this pre-processing?
(prediction complete)
Filter module(s) – require free parameters (𝛉)
(error calculated)
Error calculation module(s)
Special step pre-process

## Slide 5: Core – the fitter
Basic model:
Engine:
Fitter: Choose values of θ for which the engine produces the minimum prediction error.
= (average square difference between response and prediction)
Gradient :
How does a small change in the vector θ change E? Find that produces minimum (ie, greatest decrease in prediction error).
Keep stepping by until for all

## Slide 6: Linear STRF engine requires three modules
+
+
+
+
+
Spike-triggered average
…
…
Load
FIR
MSE

## Slide 7: model_name / keyword sequences
Model_name = “key1_key2_..._keyN”
Fitting: execute sequence key1, then key2, … then keyN
keyX is a function that can do anything, eg:
Add one or more modules to stack
Set parameters or hyperparameters
Run a fit algorithm
Eg: fb18ch100_lognn_wcg03_adp1pc_ap3z1_siglog100_fit05c
fb18ch100 – load 18 channel spectrogram, 100 Hz sampling rate
lognn – perform compression on spectrogram (1 free parm)
wcg03 – Gaussian spectral weighting to three channesl (6 free parms)
adp1pc– synaptic depression or facilitation for each of the (three) channels (3 free parms)
ap3z1– FIR pole-zero filter (4 free parms)
siglog100 – logistic sigmoid (5 free parms)
fit05c – iterative coordinate descent until 𝛥E < 10^-6

## Slide 8: Core – visualization
Spectral filter parameters
Synaptic depression parameters
FIR filter parameters
Static nonlinearity input vs. output
Predicted vs. actual response

## Slide 9: Core - browser

## Slide 10: NEMS – all the parts

## Slide 11: Near-term to-dos
Model engine
  Standard module format
  Integrate contextual variables (behavior state, pupil)
  Nested cross-validation
Fitter
  Simple gradient descent
  Iterative fitters
  Integrate with fancy fitters (eg, theano)
Web-based model & results browser, fit launcher
  Communicate data file information, pre-processing to fitter
  Model visualization tool (narf_modelpane)
  Link to cluster for fitting large datasets
  User specific batches, data sets
  Data upload/management
Core utilities for loading, plotting data and talking to celldb
  loadspikeraster – kind of replaced by
  dbgetscellfile
  raster_plot
  Etc? What would be useful to make it worth doing analysis in Python?

## Slide 12: A bunch of FIR matrices for A1 TORC STRFs
STRFs for 24 channels recorded simultaneously in A1/AAF using a fixed array of platinum-iridium electrodes.